## Slide 1: AA-HLS LAB-B #10: Matrix Multiplication
107062205 鍾宇騫
2022 / 3 / 29

## Slide 2: Index
Algorithm Introduction
Simple implementation: Brutal force
  #pragma HLS PIPELINE
  #pragma HLS RESHAPE
Complex implementation: Block matrix
  #pragma HLS DATAFLOW
  Compute optimization
Problem & Solution

## Slide 3: Algorithm Introduction
Common numerical operation for image processing, neural network, etc.
Basic multiplication and accumulation (MAC), with high parallelism.

## Slide 4: Simple Implementation with Different Pipelining
N = P = M = 32
If not set II in directive, tool will increase from 1 until meet constraint.
Pipeline | Latency | Interval | DSP
row | 45 | 45 | 3072
col | 1035 | 1036 | 96
product | 322775 | 322775 | 3

## Slide 5: HLS ARRAY_RESHAPE
Reshape array to different bandwidth memory (SRAM, register files)
#pragma HLS ARRAY_RESHAPE variable=<NAME> dim=<D>
  D = 0, reshape all
  D > 0, reshape specific dimension
Without reshape
A: dim 1, B: dim 2
A: dim 0, B: dim 0

## Slide 6: Block Matrix Multiplication
Fixed basic computing block (2x2 output matrix)
Data tiling to split a large task
Scalable computing height/width
Using hls:stream to transfer input matrix

## Slide 7: Implementation of Block MM
BLOCK_SIZE=4, SIZE=8
Input
  Stream A row (4x1)
  Stream B column (1x4)
Output
  Block matrix (4x4)
Load
  Load required rows of A
Compute
  Load required columns of B
row by row.
  MAC matrix A and B
Store
  Write result to output matrix

## Slide 8: Synthesis Result: I/O
hls:stream: Arwos and Bcols
  Data port
  Two handshaking port
Writable direct map registers: APpartial
  Two way data port
  One handshaking port
Read only registers: it

## Slide 9: Synthesis Result: Latency
Load
  Latency = Interval * SIZE(8) = 72 cycles
Compute
  Latency = Interval * SIZE(8) = 192 cycles
  MAC need to 2 adder and 1 multiplier = 3 DSP
Store
  Latency = Interval * BLOCK_SIZE(4) + overhead = 18 cycles
Loop name | Latency (cycles) | Interval (cycles) | DSP (count)
Load | 72 | 9 | 0
Compute | 192 | 24 | 3
Store | 18 | 4 | 0

## Slide 10: Compute/Store Optimization
Merger store part into compute loop to hide write out latency
Loop name | Latency (cycles) | Interval (cycles) | DSP (count)
Load | 72 | 9 | 0
Compute | 192 | 24 | 3
Store | 0 | 0 | 0

## Slide 11: Problems & Solution
Load-Store issue (Write after Read)
  SRAM: II >= 2, lower area
  Registers: II >= 1, higher are
  Tool will apply corresponding memory type based on II setting.
#pragma HLS DATAFLOW
  Task-level pipeline
  May cause R/W to the same address (port conflict)
  Manually merge write & compute loop in previous slide.

## Slide 12: GitHub Repo Link
https://github.com/andy39866821/AAHLS-LAB-B